## Slide 1: Week 11
Serial Communication.

## Slide 2: Topics
Communication theory
  Parallel vs. Serial
  Direction: Simplex, Half duplex, Full duplex
  Synchronization: Synchronous vs. Asynchronous
  Line coding
UART protocol
UART in AVR
  UART Registers
  Some programs

## Slide 3: Parallel vs. Serial
Parallel
  For short distances
  Not applicable for long distances
  More expensive
  Cross-talk problem

## Slide 4: Direction
Simplex
Half Duplex
Full Duplex

## Slide 5: Synchronization
Synchronous
Asynchronous

## Slide 6: Asynchronous serial data frame

## Slide 7: UART Protocol
Serial
Asynchronous
Full duplex

## Slide 8: USART (Universal Synchronous Asynchronous Receive Transmit)
USART devices can be used to communicate asynchronously (UART) and synchronously.
Since the synchronous capability of USART is not used nowadays, we concentrate on UART.

## Slide 9: UART in AVR
Control registers: (initialize speed, data size, parity, etc)
  UBRR, UCSRA, UCSRB, and UCSRC
Send/receive register
  UDR
Status register
  UCSRA

## Slide 10: Baud rate
System clock
UART baud rate

## Slide 11: Example: Find the UBRR value for 9600bps.
Solution:

## Slide 12: Some Standard Baud rates
1200
2400
4800
9600
19,200
38,400
57,600
115,200

## Slide 14: UCSRB
RXCIE0 (Bit 7): Receive Complete Interrupt Enable
  To enable the interrupt on the RXC0 flag in UCSR0A you should set this bit to one.
TXCIE0 (Bit 6): Transmit Complete Interrupt Enable
  To enable the interrupt on the TXC0 flag in UCSR0A you should set this bit to one.
UDRIE0 (Bit 5): USART Data Register Empty Interrupt Enable
  To enable the interrupt on the UDRE0 flag in UCSR0A you should set this bit to one.
RXEN0 (Bit 4): Receive Enable
  To enable the USART receiver you should set this bit to one.
TXEN0 (Bit 3): Transmit Enable
  To enable the USART transmitter you should set this bit to one.
UCSZ02 (Bit 2): Character Size
  This bit combined with the UCSZ1:0 bits in UCSRC sets the number of data bits (character size) in a frame.
RXB80 (Bit 1): Receive data bit 8
  This is the ninth data bit of the received character when using serial frames with nine data bits.
TXB80 (Bit 0): Transmit data bit 8
  This is the ninth data bit of the transmitted character when using serial frames with nine data bits.

## Slide 15: UCSRC
UMSEL01:00 (Bits 7:6): USART Mode Select
  These bits select the operation mode of the USART:
    00 = Asynchronous USART operation
    01 = Synchronous USART operation
    10 = Reserved
    11 = Master SPI (MSPIM)
UPM01:00 (Bit 5:4): Parity Mode
  These bits disable or enable and set the type of parity generation and check.
    00 = Disabled
    01 = Reserved
    10 = Even Parity
    11 = Odd Parity
USBS0 (Bit 3): Stop Bit Select
  This bit selects the number of stop bits to be transmitted.
    0 = 1 bit
    1 = 2 bits
UCSZ01:00 (Bit 2:1): Character Size
  These bits combined with the UCSZ02 bit in UCSR0B set the character size in a frame.
UCPOL0 (Bit 0): Clock Polarity
  This bit is used for synchronous mode.
UCSZ02 | UCSZ01 | UCSZ00 | Char. size
0 | 0 | 0 | 5-bit
0 | 0 | 1 | 6-bit
0 | 1 | 0 | 7-bit
0 | 1 | 1 | 8-bit
1 | 1 | 1 | 9-bit

## Slide 16: UDR

## Slide 17: UCSRA
RXC0 (Bit 7): USART Receive Complete 0
  This flag bit is set when there are new data in the receive buffer that are not read yet. It is cleared when the receive buffer is empty. It also can be used to generate a receive complete interrupt.
TXC0 (Bit 6): USART Transmit Complete 0
  This flag bit is set when the entire frame in the transmit shift register has been transmitted and there are no new data available in the transmit data buffer register (TXB). It can be cleared by writing a one to its bit location. Also it is automatically cleared when a transmit complete interrupt is executed. It can be used to generate a transmit complete interrupt.
UDRE0 (Bit 5): USART Data Register Empty 0
  This flag is set when the transmit data buffer is empty and it is ready to receive new data. If this bit is cleared you should not write to UDR0 because it overrides your last data. The UDRE0 flag can generate a data register empty interrupt.
FE0 (Bit 4): Frame Error 0
  This bit is set if a frame error has occurred in receiving the next character in the receive buffer. A frame error is detected when the first stop bit of the next character in the receive buffer is zero.
DOR0 (Bit 3): Data OverRun 0
  This bit is set if a data overrun is detected. A data overrun occurs when the receive data buffer and receive shift register are full, and a new start bit is detected.
PE0 (Bit 2): Parity Error 0
  This bit is set if parity checking was enabled (UPM1 = 1) and the next character in the receive buffer had a parity error when received.
U2X0 (Bit 1): Double the USART Transmission Speed 0
MPCM0 (Bit 0): Multi-processor Communication Mode 0

## Slide 18: Programing the AVR to transfer data serially
1. The UCSRB register is loaded with the value 08H, enabling the USART trans- mitter. The transmitter will override normal port operation for the TxD pin when enabled.
2. The UCSRC register is loaded with the value 06H, indicating asynchronous mode with 8-bit data frame, no parity, and one stop bit.
3. The UBRR is loaded with one of the values in Table 11-4 (if Fosc = 8 MHz) to set the baud rate for serial data transfer.
4. The character byte to be transmitted serially is written into the UDR register. 5. Monitor the UDRE bit of the UCSRA register to make sure UDR is ready for the next byte.
6. To transmit the next character, go to Step 4.

## Slide 19: Program: sending character ‘G’ continuously
#include <avr/io.h>
void usart_init (void)
{
UCSR0B = (1<<TXEN0);
UCSR0C = (1<<UCSZ01)|(1<<UCSZ00);
UBRR0L = 103; //baud rate = 9600bps
}
void usart_send (unsigned char ch)
{
while (! (UCSR0A & (1<<UDRE0))); //wait until UDR0 is empty
UDR0 = ch; //transmit ch
}
int main (void)
{
usart_init(); //initialize the USART
while(1) //do forever
usart_send ('G'); //transmit ‘G’ letter
return 0;
}

## Slide 20: Write a program to send the message "The Earth is but One Country." to the serial port continuously. Using the settings in the last example.
#include <avr/io.h>
void usart init (void)
{ UCSRB = (1<<TXEN);
UCSRC = (1<< UCSZ1) | (1<<UCSZO) | (1<<URSEL); UBRRL = 0x33; }
void usart_send (unsigned char ch)
{ while (! (UCSRA & (1<<UDRE)));
UDR = ch; }
int main (void)
{ unsigned char str[ 30]= "The Earth is but One Country. ";
unsigned char strLenght = 30;
unsigned char i = 0;
usart_init();
while (1)
{ usart_send (str[i++] ); if (i = strLenght)
i = 0; }
return 0; }

## Slide 21: Program 2: It receives bytes of data serially and puts them on Port B.
#include <avr/io.h>
int main (void)
{
DDRB = 0xFF; //Port B is output
UCSR0B = (1<<RXEN0); //initialize USART0
UCSR0C = (1<<UCSZ01)|(1<<UCSZ00);
UBRR0L = 103;
while(1)
{
while (! (UCSR0A & (1<<RXC0))); //wait until new data
PORTB = UDR0;
}
return 0;
}

## Slide 22: USB to serial converter in Arduino

## Slide 23: MAX232