## Slide 1: Week 12
SPIand I2C Communication.

## Slide 15
SPI Pins In Arduino

## Slide 16
SPI Protocol Circuits

## Slide 17: Multi-slave communication
17

## Slide 18
SPI code for Master
//SPI MASTER (ARDUINO) //SPI COMMUNICATION BETWEEN TWO ARDUINO //CIRCUIT DIGEST
#include<SPI.h> //Library for SPI #define LED 7 #define ipbutton 2 int buttonvalue; int x; void setup (void)
{ Serial.begin(115200); //Starts Serial Communication at Baud Rate 115200 pinMode(ipbutton,INPUT); //Sets pin 2 as input pinMode(LED,OUTPUT); //Sets pin 7 as Output SPI.begin(); //Begins the SPI commnuication SPI.setClockDivider(SPI_CLOCK_DIV8); //Sets clock for SPI communication at 8 (16/8=2Mhz) digitalWrite(SS,HIGH); // Setting SlaveSelect as HIGH (So master doesnt connnect with slave) }
void loop(void) { byte Mastersend,Mastereceive;
buttonvalue = digitalRead(ipbutton); //Reads the status of the pin 2
if(buttonvalue == HIGH) //Logic for Setting x value (To be sent to slave) depending upon input from pin 2 { x = 1; } else { x = 0; } digitalWrite(SS, LOW); //Starts communication with Slave connected to master Mastersend = x; Mastereceive=SPI.transfer(Mastersend); //Send the mastersend value to slave also receives value from slave if(Mastereceive == 1) //Logic for setting the LED output depending upon value received from slave { digitalWrite(LED,HIGH); //Sets pin 7 HIGH Serial.println("Master LED ON"); } else { digitalWrite(LED,LOW); //Sets pin 7 LOW Serial.println("Master LED OFF"); } delay(1000); }

## Slide 19
SPI code for Slave
Slave Arduino Code: //SPI SLAVE (ARDUINO) //SPI COMMUNICATION BETWEEN TWO ARDUINO //CIRCUIT DIGEST //Pramoth.T
#include<SPI.h> #define LEDpin 7 #define buttonpin 2 volatile boolean received; volatile byte Slavereceived,Slavesend; int buttonvalue; int x; void setup()
{ Serial.begin(115200); pinMode(buttonpin,INPUT); // Setting pin 2 as INPUT pinMode(LEDpin,OUTPUT); // Setting pin 7 as OUTPUT pinMode(MISO,OUTPUT); //Sets MISO as OUTPUT (Have to Send data to Master IN
SPCR |= _BV(SPE); //Turn on SPI in Slave Mode received = false;
SPI.attachInterrupt(); //Interuupt ON is set for SPI commnucation }
ISR (SPI_STC_vect) //Inerrrput routine function { Slavereceived = SPDR; // Value received from master if store in variable slavereceived received = true; //Sets received as True }
void loop() { if(received) //Logic to SET LED ON OR OFF depending upon the value recerived from master { if (Slavereceived==1) { digitalWrite(LEDpin,HIGH); //Sets pin 7 as HIGH LED ON Serial.println("Slave LED ON"); }else { digitalWrite(LEDpin,LOW); //Sets pin 7 as LOW LED OFF Serial.println("Slave LED OFF"); } buttonvalue = digitalRead(buttonpin); // Reads the status of the pin 2 if (buttonvalue == HIGH) //Logic to set the value of x to send to master { x=1; }else { x=0; } Slavesend=x; SPDR = Slavesend; //Sends the x value to master via SPDR delay(1000); } }

## Slide 20: SPI pins in AVR
20
MOSI (Master Out Slave In)
MISO (Master In Slave Out)
SCK
SS

## Slide 21: AVR registers
21
Control register:
  SPCR (SPI Control Register)
Status Register:
  SPSR (SPI Status Register)
Data Register:
  SPDR (SPI Data Register)

## Slide 22: SPSR (SPI Status Register)
22
SPIF (SPI Interrupt Flag)
  A serial transfer is completed.
  The SS pin is driven low in slave mode
WCOL (Write Collision)
SPI2X (Double SPI Speed)

## Slide 23: SPCR
23
SPIE (SPI Interrupt Enable)
SPE (SPI Enable)
DORD (Data Order)
MSTR (Master)
CPOL (Clock Polarity)
CPHA (Clock Phase)
SPR1, SPR0 :SPI Clock Rate
SPI2X | SPR1 | SPR0 | SCK Freq.
0 | 0 | 0 | Fosc/4
0 | 0 | 1 | Fosc/16
0 | 1 | 0 | Fosc/64
0 | 1 | 1 | Fosc/128
1 | 0 | 0 | Fosc/2 (not recommended)
1 | 0 | 1 | Fosc/8
1 | 1 | 0 | Fosc/32
1 | 1 | 1 | Fosc/64
CPOL | CPHA | Data Read and Change Time | SPI Mode
0 | 0 | Read on rising edge, changed on a falling edge | 0
0 | 1 | Read on falling edge, changed on a rising edge | 1
1 | 0 | Read on falling edge, changed on a rising edge | 2
1 | 1 | Read on rising edge, changed on a falling edge | 3

## Slide 24
SPCR

## Slide 25: Program 1: Sending ‘G’ through SPI as a master
25
#include <avr/io.h>
#define MOSI 3
#define SCK 5
#define SS 2
int main (void)
{
DDRB = (1<<MOSI)|(1<<SCK)|(1<<SS); //MOSI and SCK are output
DDRD = 0xFF; //Port D is output
SPCR = (1<<SPE)|(1<<MSTR)|(1<<SPR0); //enable SPI as master
while(1) //do for ever
{
PORTB &= ~(1<<SS); //enable slave device
SPDR = 'G'; //start transmission
while(!(SPSR & (1<<SPIF))); //wait transfer finish
PORTD = SPDR; //move received data to PORTD
PORTB |= (1<<SS); //disable slave device
}
return 0;
}

## Slide 26: Program 2: Sending ‘G’ through SPI as a slave
26
#include <avr/io.h>
#define MISO 4
int main (void)
{
DDRD = 0xFF; //Port D is output
DDRB = (1<<MISO); //MISO is output
SPCR = (1<<SPE); //enable SPI as slave
while(1)
{
SPDR = 'G';
while(!(SPSR &(1<<SPIF))); //wait for transfer finish
PORTD = SPDR; //move received data to PORTD
}
return 0;
}

## Slide 27
Embedded Systems Design
Inter-Integrated Circuit (I2C)

## Slide 28: I2C bus
Communication with the accelerometer
  Read acceleration values and configure interrupts
Pros
  Two wires bus that can connect multiple peripherals with the MCU
Cons
  Overhead is significantly higher, and bus is slower

## Slide 29: I2C Details
Two lines
  Serial data line (SDA)
  Serial clock line (SCL)
Only two wires for connecting multiple devices

## Slide 30: I2C Details

## Slide 31: I2C Details

## Slide 32: I2C Details
Each I2C device recognized by a unique address
Each I2C device can be either a transmitter or receiver
I2C devices can be masters or slaves for a data transfer
  Master (usually a microcontroller): Initiates a data transfer on the bus, generates the clock signals to permit that transfer, and terminates the transfer
  Slave: Any device addressed by the master at that time

## Slide 33: How can any device transfer or receive on the same two wires?
Pull ups and high-impedance mode pins
  Wires default to being “on”, any device can make a wire go “off”.
  This is super clever. SPI and UART can’t do this, why?

## Slide 34: Start and Stop Condition

## Slide 35: Acknowledge (ACK) and Not Acknowledge (NACK)
A transition of the data line while the clock line is high
is defined as either a start
or a stop condition.
Both start and stop conditions are generated by the bus master
The bus is considered busy after a start condition, until a stop condition occurs

## Slide 36: Bit Transfer on the I2C Bus

## Slide 37: Start and Stop Conditions
A transition of the data line while the clock line is high is defined as either a start or a stop condition.
Both start and stop conditions are generated by the bus master
The bus is considered busy after a start condition, until a stop condition occurs
Start Condition
Stop Condition
SCL
SCL
SDA
SDA

## Slide 38: I2C Addressing
Each node has a unique 7 (or 10) bit address
Peripherals often have fixed and programmable address portions
Addresses starting with 0000 or 1111 have special functions:-
  0000000 Is a General Call Address
  0000001 Is a Null (CBUS) Address

## Slide 39: I2C-Connected System
Example I2C-connected system with two microcontrollers
(Source: I2C Specification, Philips)