## Slide 1: Week 13
Analog to Digital conversion
&
Pulse Width Modulation

## Slide 2: Analog vs. Digital Signals

## Slide 3: What is an ADC?
An analog-to-digital converter (ADC, A/D or A2D) converts an analog signal to a digital signal, and a digital-to-analog converter (DAC, D/A or D2A) does the opposite.
An embedded system uses the ADC to collect information about the external world.
The input signal is usually an analog voltage, and the output is a binary number.
Why we need ADC Interfacing?

## Slide 4
Analog-to-Digital Converters (ADCs) are used to convert analog signals into digital representations that can be communicated and processed using digital logic.
A physical quantity which is analog in nature is converted to electrical signals using a device called transducers.
Transducers are also referred to as sensors.
Sensors produce an output that is voltage or current. Therefore, we need an ADC to translate the analog signals to digital numbers so that micro-controller can read and process them.
What is an ADC Interfacing?

## Slide 5
Such conversions are necessary because, while embedded systems deal with digital values, an embedded system’s surroundings typically involve many analog signals.
Analog refers to continuously-valued signal, such as temperature or speed represented by a voltage between 0 and 100, with infinite possible values in between.
Digital refers to discretely-valued signals, such as integers, and in computing systems, these signals are encoded in binary. By converting between analog and digital signals, we can use digital processors in an analog environment.
Why we need ADC Interfacing?

## Slide 6
The capacity of an ADC to encode an analogue input is 2 raise to the power n, where n= no. of bits of ADC.
The resolution of a DAC or ADC is defined as Vmax/(2n-1), representing the number of volts between successive digital encodings.
Example:
An ADC with a resolution of 8 bits can encode an analog input to one in 256 different levels (28 = 256). The values can represent the ranges from 0 to 255 (i.e. unsigned integer) or from −128 to 127 (i.e. signed integer), depending on the application.
How many ADC bits are required

## Slide 7: ADC
ADC
Vref
Output
Vin
n
(binary number)

## Slide 8: ADC in AVR

## Slide 9: ADC in AVR

## Slide 10: ADMUX
MUX0-MUX1: input select
ADLAR:
  0: right adjust the result
  1: left adjust the result
REFS1-REFS0: Vref selection

## Slide 11: ADCSA

## Slide 12: Steps in programming ADC
1. Make the pin for the selected ADC channel an input pin.
2. Turn on the ADC module
3. Select the conversion speed
4. Select voltage reference and ADC input channels.
5. Activate the start conversion bit by writing a one to the ADSC bit of ADCSRA.
6. Wait for the conversion to be completed by polling the ADIF bit in the ADCSRA register.
7. After the ADIF bit has gone HIGH, read the ADCL and ADCH registers to get the digital data output.
8. If you want to read the selected channel again, go back to step 5.
9. If you want to select another Vref source or input channel, go back to step 4.

## Slide 13: Sensors
Sensor: Converts a physical signal (e.g. light, temperature, humidity, etc.) to an electrical signal (e.g. resistance, voltage, current, capacitance, etc)

## Slide 14: LM35 & LM34 (Temperature Sensors)
LM35 and LM34:
  convert temp. to voltage
  10mV for each degree

## Slide 15
LM35 (Temperature Sensors)

## Slide 16
#define LM35 A0
#define RED 7
#define GREEN 6
float lm_value;
float tempc;
void setup() {
Serial.begin(9600);
pinMode(RED, OUTPUT);
pinMode(GREEN, OUTPUT);
}
void loop() {
lm_value = analogRead(LM35);
tempc = (lm_value * 500) / 1023;
Serial.println(tempc);//Temperature in Celcius
//Condition
if (tempc > 60) {
digitalWrite(RED, HIGH);
digitalWrite(GREEN, LOW);
}
else {
digitalWrite(GREEN, HIGH);
digitalWrite(RED, LOW);
}
delay(100);
}
Temperature Sensors

## Slide 17
17
Soil Moisture

## Slide 18: Soil Sensor Programming
const int sensor_pin = A1; /* Soil moisture sensor O/P pin */
void setup(){
Serial.begin(9600); /* Define baud rate for serial communication */
}
void loop(){
float moisture_percentage;
int sensor_analog;
sensor_analog = analogRead(sensor_pin);
moisture_percentage = ( 100 - ( (sensor_analog/1023.00) * 100 ) ); Serial.print("Moisture Percentage = ");
Serial.print(moisture_percentage);
Serial.print("%\n\n");
delay(1000);
}

## Slide 19
19
void setup() {
Serial.begin(9600);
}
void loop() {
int rawValue = analogRead(A0);
Serial.println(rawValue);
delay(100);
}
Voltage Level using Variable Resistor

## Slide 20
20
void setup() {
Serial.begin(9600);
}
void loop() {
int rawValue = analogRead(A0);
float voltage = rawValue * (5.0 / 1023.0);
Serial.print(voltage);
Serial.println(" Volts");
delay(100); }
rawValue=map(rawValue, sensorMin, sensorMax, 0, 255);
Voltage Level using Variable Resistor

## Slide 21
PWM

## Slide 22
Control Signal Relationship

## Slide 23
Pulse width modulation (PWM) is a form of digital to analogue conversion (DAC).
PWM varies the time for which the output voltage is set high (the duty cycle) in a set frequency. Output devices like DC motors interpret this as the average voltage during each period. The bars in the diagram below show how the pulse widths in this signal vary. Each pulse is 10 ms apart, for example, a 1 ms pulse below would be a 10% duty cycle (1 ms/10 ms).
What is the frequency of this PWM signal?
Calculate the % duty cycle during each period, and the average voltage this produces each time.
What duty cycle would be needed to create the following average voltages? 1.2 V, 3.5 V, 4.8 V
This controller has 8-bit resolution (0 to 255). What is the resolution of the PWM output, in volts?
What is pulse width modulation?

## Slide 24
The frequency of the PWM signal is 100 Hz (1/10 ms = 100)
Duty cycles:
1.2 V: 24%, or 2.4 ms (1.2 V/5 V x 100% = 24%)
3.5 V: 70%, or 7 ms
4.8 V: 96%, or 9.6 ms
The resolution of the PWM output is 5 Volts / 256 steps = 0.02 V to 2 decimal places.
What is happening if the duty cycle is set to zero or 100%?
More generally, what is happening if the duty cycle stays the same?
How could PWM control the speed of a motor?
What is pulse width modulation?

## Slide 25
A CNC machine status light can be red, amber or green.
A microcontroller changes the status of the red, green or blue emitters in an RGB LED.
Each emitter can be on, dimmed (50% duty cycle) or off.
First, think about what PWM signal to each emitter will create a red, yellow or green light. Then, consider whether you need to send a 50% duty cycle signal to the red or green emitter, while leaving the other on 100%, to change yellow to amber. Sketch on the activity sheet what PWM signals would make the light cycle through red, amber and green statuses.
Applying pulse width modulation: RGB LEDs

## Slide 26
Complete the table on the activity sheet to show the duty cycles for a range of tool head motor speeds.
The CNC tool head motor has an operating speed of 0 to 12,000 rpm.
The microcontroller will operate a higher power PWM circuit to control the motor speed.
This PWM circuit will operate at a frequency of 50 kHz.
Applying pulse width modulation: DC motors

## Slide 27
The tool head is controlled by a servo motor that can move from 0 to 180, with a resting position of 90.
The PWM signal for the servo has a frequency of 100 Hz.
The pulse width for the three key positions is 1 ms (0), 1.5 ms (90) and 2 ms (180).
Calculate the pulse width for the intermediate positions listed on the activity sheet.
If the microcontroller has an 8-bit (256 step) resolution, what is in principle the smallest increment by which the servo motor can rotate?
Applying pulse width modulation: servo motors

## Slide 29
  Use Pulse Width Modulation (PWM) to approximate
    Digital outputs are capable of 0V or 5V
    Over a fraction (ton) of a time period tcycle, keep pin at 5V, the rest of the time, at 0V
      Average voltage is proportional to ton/tcycle, called the ‘Duty Cycle’
Application
Identify how PWM can control a range of devices including LEDs, DC motors and servo motors.
Make calculations to generate the right PWM signal to obtain desired results.
Pulse width modulation

## Slide 30: Arduino analogWrite( )
analogWrite(pin, value);
  0  value  255
    0% duty cycle --> 0 V --> analogWrite(pin, 0);
    100% duty cycle --> 5 V --> analogWrite(pin, 255);

## Slide 31: Analog Output Example
Fade the red LED in, then out
  duty cycle is incremented then decremented
  256 steps
    0% to 100%
const byte ledPin = 3; // red RGB LED on Experimenter
const byte FADE_MAX = 255; // max value for setting duty cycle
const byte FADE_INC = 5; // increment for changing duty cycle
void setup()
{
pinMode(ledPin, OUTPUT);
}
void loop()
{
int fadeValue; // PWM value
// fade in from min to max in increments of 5 points:
for(fadeValue = 0 ; fadeValue <= FADE_MAX; fadeValue +=FADE_INC)
{
analogWrite(ledPin, fadeValue); // sets the value (range from 0 to 255):
}
// fade out from max to min in increments of 5 points:
for(fadeValue = FADE_MAX; fadeValue >= 0; fadeValue -=FADE_INC)
{
analogWrite(ledPin, fadeValue); // sets the value (range from 0 to 255):
}
}

## Slide 32
int redPin= 6;
int greenPin = 5;
int bluePin = 4;
void setup() {
pinMode(redPin, OUTPUT);
pinMode(greenPin, OUTPUT);
pinMode(bluePin, OUTPUT);
}
void loop() {
setColor(255, 0, 0); // Red Color
delay(1000);
setColor(0, 255, 0); // Green Color
delay(1000);
setColor(0, 0, 255); // Blue Color
delay(1000);
setColor(255, 255, 255); // White Color
delay(1000);
setColor(170, 0, 255); // Purple Color delay(1000); } void setColor(int redValue, int greenValue, int blueValue) { analogWrite(redPin, redValue);
analogWrite(greenPin, greenValue);
analogWrite(bluePin, blueValue); }

## Slide 33
Robotics Car using DC Motor

## Slide 34
DC Motor speed Forward and Reverse direction

## Slide 35
Car Moves using Joystick

## Slide 37
void setup() {
// Set up left motor pins
pinMode(leftMotorIn1, OUTPUT);
pinMode(leftMotorIn2, OUTPUT);
pinMode(leftMotorEn, OUTPUT);
// Set up right motor pins
pinMode(rightMotorIn1, OUTPUT);
pinMode(rightMotorIn2, OUTPUT);
pinMode(rightMotorEn, OUTPUT);
// Set up button pins
pinMode(forwardButton, INPUT_PULLUP);
pinMode(reverseButton, INPUT_PULLUP);
pinMode(leftButton, INPUT_PULLUP);
pinMode(rightButton, INPUT_PULLUP);
}
// Define motor control pins for left motor
int leftMotorIn1 = 10;
int leftMotorIn2 = 9;
int leftMotorEn = 8;
// Define motor control pins for right motor
int rightMotorIn1 = 6;
int rightMotorIn2 = 5;
int rightMotorEn = 7;
// Define button pins
int forwardButton = 1;
int reverseButton = 2;
int leftButton = 3;
int rightButton = 4;

## Slide 38
void moveForward() {
digitalWrite(leftMotorEn, HIGH);
digitalWrite(leftMotorIn1, HIGH);
digitalWrite(leftMotorIn2, LOW);
digitalWrite(rightMotorEn, HIGH);
digitalWrite(rightMotorIn1, HIGH);
digitalWrite(rightMotorIn2, LOW);
}
void moveReverse() {
digitalWrite(leftMotorEn, HIGH);
digitalWrite(leftMotorIn1, LOW);
digitalWrite(leftMotorIn2, HIGH);
digitalWrite(rightMotorEn, HIGH);
digitalWrite(rightMotorIn1, LOW);
digitalWrite(rightMotorIn2, HIGH);
}
void turnLeft() {
digitalWrite(leftMotorEn, HIGH);
digitalWrite(leftMotorIn1, LOW);
digitalWrite(leftMotorIn2, HIGH);
digitalWrite(rightMotorEn, HIGH);
digitalWrite(rightMotorIn1, HIGH);
digitalWrite(rightMotorIn2, LOW);
}
void turnRight() {
digitalWrite(leftMotorEn, HIGH);
digitalWrite(leftMotorIn1, HIGH);
digitalWrite(leftMotorIn2, LOW);
digitalWrite(rightMotorEn, HIGH);
digitalWrite(rightMotorIn1, LOW);
digitalWrite(rightMotorIn2, HIGH);
}
void stopMotors() {
digitalWrite(leftMotorEn, LOW);
digitalWrite(rightMotorEn, LOW);
}

## Slide 39
void loop() {
// Check the status of each button
if (digitalRead(forwardButton) == LOW) {
moveForward();
} else if (digitalRead(reverseButton) == LOW) {
moveReverse();
} else if (digitalRead(leftButton) == LOW) {
turnLeft();
} else if (digitalRead(rightButton) == LOW) {
turnRight();
} else {
stopMotors();
}
}

## Slide 40: Timer0 Review
40
TCNT0
TCCR0A
TOV0
OCR0B
=
OCF0B
TCCR0B
OCR0A
=
OCF0A

## Slide 41
WGM02 WGM01 WGM00 Comment
0 0 0 Normal
0 0 1 Phase correct PWM
0 1 0 CTC (Clear Timer on Compare Match)
0 1 1 Fast PWM
1 0 0 Reserved
1 0 1 Phase correct PWM
1 1 0 Reserved
1 1 1 Fast PWM
Timer Mode (WGM)

## Slide 42: Fast PWM mode
42
Similar to Normal mode but OCR0x are buffered.
0xFF
TCNT0
0
TOV
TOV
TOV
time
0
TOV0:
1
0
1
2
FE
FF
TOV0 = 1
TCNT0
TOV0
OCR0x
=
OCF0x
OCR0x-BUF
TOV0

## Slide 43: Phase Correct PWM mode
43
Goes up and down like a yo-yo
When TCNT becomes zero, the TOV0 flag sets.
0xFF
TCNT0
0
time
0
TOV0:
1
TCNT0
TOV0
OCR0x
=
OCF0x
OCR0x-BUF
TCNT0=0xFF
TOV
1
2
TOV0 = 1
0
FE
FF

## Slide 44
44
Compare Output Mode (COM)
CTC or Normal (Non PWM)
Fast PWM
Phase Correct PWM
COM0x1 | COM0x0 | Description
0 | 0 | Normal port operation, OC0 disconnected
0 | 1 | Toggle OC0 on compare match
1 | 0 | Clear OC0 on compare match
1 | 1 | Set OC0 on compare match
COM0x1 | COM0x0 | Description
0 | 0 | Normal port operation, OC0 disconnected
0 | 1 | Reserved
1 | 0 | Clear OC0 on compare match, set OC0 at TOP.
1 | 1 | Set OC0 on compare match, clear OC0 at TOP.
COM0x1 | COM0x0 | Description
0 | 0 | Normal port operation, OC0 disconnected
0 | 1 | Reserved
1 | 0 | Clear OC0 on compare match when up-counting. Set OC0 on compare match when down-counting.
1 | 1 | Set OC0 on compare match when up-counting. Clear OC0 on compare match when down-counting.

## Slide 45: Fast PWM Calculations
45
Fast PWM
Duty cycle = changeable (0% to 100%)
Frequency = selectable between limited choices
TCNT0
0
OCR0x
0xFF
OC0x
OC0x
0xFF
TCNT0
0
OCR0x
OC0x
OC0x
COM=2
COM=3
N(256)
fclk
FOC0=
COM=2
COM=3
COM=2
COM=3

## Slide 46: Assuming XTAL = 16 MHz, make the following pulse duty cycle = 75% and frequency = 62.500KHz
46
DDRD |= (1<<6); //PD6 as output
OCR0A = 191;
TCCR0A = (1<<COM0A1)|(1<<WGM01)|(1<<WGM00);
TCCR0B = 0x01; //N = 1 (no prescaler)
fclk
N(256)
FOC0=
16MHz
N(256)
62.500KHz=
N =
16MHz
62.500K*256
SBI DDRD, 6
LDI R20,191
OUT OCR0A,R20
LDI R20, (1<<COM0A1)|(1<<WGM01)|(1<<WGM00)
OUT TCCR0A,R20
LDI R20,0x01
OUT TCCR0B,R20
=1
75/100 = (OCR0x+1)/256  OCR0x+1 = 192  OCR0x = 191